Table 1. ИХ-1, ИХ-2 evaporators and КХ condensers’ basic parameters.

| Parameter | Values |
| --- | --- |
|  | ИХ-1 | ИХ-2 | КХ |
| Heat exchange surface, m2 | 21-1323 | 22-1485 |
| Housing inner diameter, mm (sheet steel) | 400; 600; 800; 1000; 1200; 1400; 1600; 1800; 2000. |
| Temperature of heat exchange media , (T(5) (С, in tubes | from - 20 from - 60 up to + 60 up to + 60 | from - 20 up to + 50 |
| In housing | from - 40 from - 60 up to + 40 up to + 40 | From 0 up to + 100 |
| Nominal pressure, MPa, no more, in tubes of equipment of diameter, mm 400-1600 1800-2000 | Up to 0,6 | 1,0;1,6;2,5 1,0;1,6 | 0,6 |
| In houising | 1,6 | 2,5 | 2,0 |
| Heat exchange tubes length, mm of equipment of diameter, mm 400 | 3000 |
| 600; 800 | 3000; 4000 |
| 1000 | 3000; 4000; 6000 |
| 1200;1400 | 4000; 6000 |
| 1600;1800; 2000 | 6000 |
| Outer diameter and wall thickness of heat exchange tube, mm | 25(2 |
| Number of strokes through tube for the equipment of diameter, mm 400 | 2 |
| 600 | 2; 6 |
| 800-1400 | 2; 4; 6; 8 |
| 1600-2000 | 2; 4; 6 |
| Diagram and step of heat exchange tube installation at tube plates, mm | Diagram – at tops of equiangular triangles. Step – 32. |
| Note: It is allowed to manufacture the evaporators and condenser’ housing from tude with outer diameter of 426 и 630 mm. |

Evaporator  ИХ-1

Figure1. ИХ-1 Evaporator. 1 – distribution box cover; 2 – distribution box; 3 – casing; 4 – support; 5 – oil colllector; 6 – heat exchange pipe; 7 –  casing cover; 8 – steam dome. DyА –product entryy; DyБ (Dy50 mm)– drainage, blowing; DyВ – cooling agent stem exit; DyГ (Dy40 mm) – vacuum pressure gauge; DyД – relief valve; DyЕ (Dy50 mm) – level indicator; DyЖ (Dy50 mm) – cooling agent outlet; DyК – cooling agent inlet; DyЛ – product exit; DyМ (Dy50 mm) – impurities outlet.

Table 2 – Basic sizes of ИХ-1 evaporators.

| Внутренний диаметр кожуха, Dв, mm | L, mm no more | l0, mm | l1, mm | l2, mm | H, mm | H1, mm | h2, mm | В, mm no more |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 400 | 3600 | – | 210 | 175 | 1260 | 363 | 800 | 630 |
| 600 | 3690 |  | 230 | 195 | 1480 | 530 | 890 | 830 |
|  | 4690 |  |  |  |  |  |  |  |
| 800 | 3810 |  | 265 | 225 | 1810 | 627 | 1100 | 1040 |
|  | 4810 |  |  |  |  |  |  |  |
| 1000 | 4040 |  | 330 | 275 | 2100 | 729 | 1260 | 1240 |
|  | 5040 |  |  |  |  |  |  |  |
|  | 7040 |  |  |  |  |  |  |  |
| 1200 | 5220 | 2000 | 400 | 345 | 2510 | 831 | 1560 | 1450 |
|  | 7220 | 3000 |  |  |  |  |  |  |
| 1400 | 5470 | 2000 | 465 | 380 | 2800 | 990 | 1730 | 1650 |
|  | 7520 | 3000 | 490 | 425 |  |  |  |  |
| 1600 | 7590 |  | 590 |  | 3150 | 1090 | 1950 | 1860 |
| 1800 | 7800 |  | 690 | 475 | 3400 | 1190 | 2100 | 2060 |
| 2000 | 8020 |  | 760 | 560 | 3700 | 1290 | 2300 | 2260 |

Note: ИХ-1 evaporators are designed for operation at nominal pressure in pipes of 0.6 MPа, in casing 1.6 MPa.

Evaporator ИХ-2

Figure2. ИХ-2 Evaporator. 1 – distribution box cover; 2 – distribution box; 3 – casing; 4 – support; 5 – oil colllector; 6 – heat exchange pipe; 7 –  casing cover; 8 – steam dome. DyА –product entryy; DyБ (Dy50 mm)– drainage, blowing; DyВ – cooling agent stem exit; DyГ (Dy40 mm) – vacuum pressure gauge; DyД – relief valve; DyЕ (Dy50 mm) – level indicator; DyЖ (Dy50 mm) – cooling agent outlet; DyК – cooling agent inlet; DyЛ – product exit; DyМ (Dy50 mm) – impurities outlet.

Table 3 – Основные размеры испарителей ИХ-2.

| Внутренний диаметр кожуха, Dв, mm | Давление в трубах Ру, МПа no more | L, mm no more | l0, mm | l1, mm | l2, mm | H, mm | H1, mm | h2, mm | V, mm no more |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 400 | 1,0; 1,6 | 3680 | 1500 | 260 | 500 | 1260 | 363 | 800 | 630 |
|  | 2,5 | 3690 |  |  |  |  |  |  |  |
| 600 | 1,0; 1,6 | 3830 |  | 320 |  | 1480 | 530 | 890 | 830 |
|  |  | 4830 | 2000 |  | 800 |  |  |  |  |
|  | 2,5 | 3850 | 1500 |  | 500 |  |  |  |  |
|  |  | 4850 | 2000 |  | 800 |  |  |  |  |
| 800 | 1,0 | 4360 | 1500 | 685 | 500 | 1810 | 627 | 1100 | 1040 |
|  |  | 5360 | 2000 |  | 800 |  |  |  |  |
|  | 1,6 | 4370 | 1500 |  | 500 |  |  |  |  |
|  |  | 5370 | 2000 |  | 800 |  |  |  |  |
|  | 2,5 | 4390 | 1500 | 695 | 500 |  |  |  |  |
|  |  | 5390 | 2000 |  | 800 |  |  |  |  |
| 1000 | 1,0 | 4500 | 1500 | 755 | 500 | 2100 | 729 | 1260 | 1240 |
|  |  | 5500 | 2000 |  | 800 |  |  |  |  |
|  |  | 7500 | 3000 |  | 1200 |  |  |  |  |
|  | 1,6 | 4510 | 1500 |  | 500 |  |  |  |  |
|  |  | 5510 | 2000 |  | 800 |  |  |  |  |
|  |  | 7510 | 3000 |  | 1200 |  |  |  |  |
|  | 2,5 | 4560 | 1500 | 820 | 500 |  | 779 |  | 1260 |
|  |  | 5560 | 2000 |  | 800 |  |  |  |  |
|  |  | 7560 | 3000 |  | 1200 |  |  |  |  |
| 1200 | 1,0 | 5660 | 2000 | 840 | 800 | 2510 | 831 | 1560 | 1450 |
|  |  | 7660 | 3000 |  | 1200 |  |  |  |  |
|  | 1,6 | 5690 | 2000 |  | 800 |  |  |  |  |
|  |  | 7690 | 3000 |  | 1200 |  |  |  |  |
|  | 2,5 | 5710 | 2000 | 855 | 800 |  | 879 |  | 1480 |
|  |  | 7710 | 3000 |  | 1200 |  |  |  |  |
| 1400 | 1,0 | 5850 | 2000 | 930 | 800 | 2800 | 990 | 1730 | 1650 |
|  |  | 7850 | 3000 |  | 1200 |  |  |  |  |
|  | 1,6 | 5910 | 2000 | 955 | 800 |  |  |  |  |
|  |  | 7910 | 3000 |  | 1200 |  |  |  |  |
|  | 2,5 | 5970 | 2000 | 990 | 800 |  |  |  | 1680 |
|  |  | 7970 | 3000 |  | 1200 |  |  |  |  |
| 1600 | 1,0 | 8070 |  | 1035 |  | 3150 | 1090 | 1950 | 1860 |
|  | 1,6 | 8130 |  | 1060 |  |  |  |  |  |
|  | 2,5 | 8220 |  | 1110 |  |  |  |  | 1880 |
| 1800 | 1,0 | 8350 |  | 1175 |  | 3400 | 1190 | 2100 | 2060 |
|  | 1,6 | 8430 |  | 1215 |  |  |  |  |  |
| 2000 | 1,0 | 8650 |  | 1325 |  | 3700 | 1290 | 2300 | 2260 |
|  | 1,6 | 8730 |  | 1365 |  |  |  |  |  |

Condenser КХ

Figure3. Конденсатор КХ. 1 – крышка распределительной камеры; 2 – распределительная камера; 3 – кожух; 4 – опора; 5 – маслосборник; 6 – труба теплообменная; 7 – крышка кожуха. DyА – выход воды; DyБ – вход паров хладагента; DyВ (Dy10 mm) – вентиль для продувки; DyГ – предохранительный клапан; DyД (Dy40 mm) – мановакууметр; DyE – продувка, отбор паров; DyЖ – выход жидкого хладагента; DyK (Dy50 mm) – указатель уровня; DyЛ (Dy50 mm)  – слив хладагента; DyM – вход воды; DyH (Dy50 mm) – слив примесей.

Table 4 – Основные размеры конденсаторов КХ, mm.

| Внутренний диаметр кожуха, Dв, mm | L, mm no more | l0, mm | l1, mm | l2, mm | H, mm | H1, mm | h2, mm | В, mm no more |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 400 | 3680 | 1500 | 250 | 500 | 820 | 363 | 320 | 630 |
| 600 | 3900 |  | 310 |  | 1120 | 530 | 420 | 830 |
|  | 4900 | 2000 |  | 800 |  |  |  |  |
| 800 | 3970 | 1500 | 315 | 500 | 1340 | 627 | 530 | 1040 |
|  | 4970 | 2000 |  | 800 |  |  |  |  |
| 1000 | 4210 | 1500 | 380 | 500 | 1570 | 729 | 630 | 1240 |
|  | 5210 | 2000 |  | 800 |  |  |  |  |
|  | 7210 | 3000 |  | 1200 |  |  |  |  |
| 1200 | 5400 | 2000 | 450 | 800 | 1780 | 831 | 740 | 1450 |
|  | 7400 | 3000 |  | 1200 |  |  |  |  |
| 1400 | 5630 | 2000 | 575 | 800 | 2060 | 990 | 840 | 1650 |
|  | 7630 | 3000 |  | 1200 |  |  |  |  |
| 1600 | 7690 |  | 640 |  | 2290 | 1090 | 940 | 1860 |
| 1800 | 7950 |  | 760 |  | 2490 | 1190 | 1050 | 2060 |
| 2000 | 8220 |  | 860 |  | 2690 | 1290 | 1150 | 2260 |

Примечание: конденсаторы предназначены для работы при условном давлении в трубах 0,6 МПа в кожухе 2,0 МПа.