Table 1 – Basic parameters of thermosyphon evaporators

| Parameters | Values for evaporators types |
| --- | --- |
|  | INT | IKT | IPT |
| Heat exchange surface, m2 | 40…1240 | 40…464 |
| Housing inner diameter, mm (sheet steel) | 600; 800; 1000; 1200; 1400; 1600; 1800; 2000; 2200 | 600; 800; 1000; 1200; 1400 | 600; 800; 1000; 1200 |
| Temperature of heating and evaporated medium (Т(5), °С | From - 70 up to + 350 | From - 70 up to + 450 |
| Nominal pressure, MPa, no more, in tubes of equipment of diameter, mm 600…1000 | 1,0; 1,6; 2,5 | 1,0; 1,6 | 1,6; 2,5; 4,0; 6,3 |
| 1200 | 1,0; 1,6; 2,5 |  |  |
| 1400 |  |  | – |
| 1600…2000 |  | – |  |
| 2200 | 1,0; 1,6 |  |  |
| In housing for equipment of diameter, mm 600…1000 | 1,0; 1,6; 2,5; 4,0 | 1,0; 1,б | 1,6; 2,5 |
|  | 1200 | 1,0; 1,6; 2,5 |  |  |
|  | 1400 |  |  | – |
|  | 1600…2000 |  | – |  |
|  | 2200 | 1,0; 1,6 |  |  |
| Heat exchange tubes’ length, mm for equipment of diameter, mm 600…1000 1200…2200 | 2000; 3000; 4000 3000; 4000 | 3000; 6000 |
| Outer diameter and wall thickness of heat exchange tube, mm | 25(2 | 25(2; 25(2,5 |
| Number of strokes through tube | 1 | 2; 4; 6 |
| Diagram and step of heat exchange tube installation at tube plates, mm | Diagram – at tops of equiangular triangles. Step – 32. |

Figure 1. The evaporators of ИНT and ИКТ type design 1. DyА – product enter (exit); DyБ – product enter; DyВ – exit of product steams.

Figure 2.

The evaporators of ИНТ and ИКТ type design 2. DyА – steams

enter; DyБ – product enter; DyВ – exit of product stems; DyГ – exit of condensate.